Soft errors and reliability
Ph.D R&D Project
Nanditha Rao
under the guidance of
Prof. Madhav. P. Desai
Dept of Electrical Engineering
IIT Bombay
April 2012

---
Agenda
- Objective
- Soft errors and their impact
- Redundancy techniques
- Outline of the simulation setup
- PIC architecture in brief
- Implementation details
- Simulation results
- Conclusion

---
Objective
To study the impact of soft errors on processor execution and build reliability in the processor to reduce the impact

---
Soft error: physics
Alpha particles
High energy neutrons
A new physical mechanism for soft errors in dynamic memories,Timothy C. May, Murray H. Woods,Reliability Physics Symposium, 1978.

---
Soft error trends
SER per bit
System SER trend in SRAM
DRAM cell upset trending down
Robert. Baumann, “The Impact of Technology Scaling on Soft Error Rate Performance and Limits to the Efficacy of Error Correction,” Proc. IEEE Int’l Electronic Device Meeting, pp. 329-332, Dec. 2002.
10000 FIT/bit => 0.1 error/year per CPU
Charles Slayman, “Soft Error Trends and Mitigation Techniques in Memory Devices”, Ops A La Carte, Jan 2011
SRAM (128Mb): 20000 FIT/CPU -> 2 errors/year per CPU
DRAM:(2Tb): 2000 FIT -> 0.2 errors/year
[Speaker Notes: ER/chip of SRAM shows lit- tle increase as feature size decreases. Furthermore, pipeline depth has no noticeable effect, since the percentage of chip area allocated to SRAM changes very little. SER/chip in latches increases only slightly for all pipeline depths, a combined effect of the relatively constant SER/latch and the increasing number of latches at smaller feature sizes. SER/chip of latches increases for deeper pipelines, due solely to the greater number of latches required for deeper pipeline microarchitectures. SER/chip in combinational logic increases dramatically from 600nm to 50nm, from 10 to approximately 1.0, or eight orders of magnitude. This is simply the composition of a 10 increase in SER per individual logic chain and more than 100 increase in logic chains per chip. At 50nm and a 6 FO4 pipeline, the SER per chip of logic exceeds that of latches, and is within two orders of magnitude of the SER per chip of unprotected memory elements. 2nd figure: On the X-axis we plotted the number of errors at the nominal process voltage 1.2V. The Y-axis shows the equivalent meas- urements, i.e. for the same diode type and size, at voltages other than 1.2V. A single voltage scaling coefficient applied to both the NMOS and PMOS diodes and all sizes. The fined solid lines show that scaling of voltage from 1.2V to OAV, 1:2V to l.OV, and 1.2V to 1.3V resulted in scaling of SER by +loo%, +33%, and -9%, respectively. On the average, the SER increased by 18% for every 10% reduction in voltage.]

---
Mitigation techniques
- Process/material improvements
- Micro solutions
  - Parity and Error correcting codes
- Macro solutions
  - Cycle-by-cycle lockstepping
  - CPU or thread mirroring
    - Identify the offending processor
    - Double/Triple modular redundancy
  - Exception Handling
  - Checkpointing (recover from control flow errors)
  - Multicore
[Speaker Notes: Two broad solutions for fault detection include cycle-by-cycle lockstepping of identical processor pipelines [15] and redundant multithreading (RMT) [9][1]. In cycle-by-cycle lockstepping, the same program is run on identical pipelines whose outputs are checked for mismatches every cycle. In RMT, outputs of selected committed instructions are checked for mismatch at commit point of instructions [12]. But, unlike lockstepping, RMT does not require the two threads to be cycle-synchronized Arithmetic exceptions like overflow and divide-by-0 often can be ignored. For memory access exceptions, a default value can be returned in case of a load and the operation can be skipped in case of a store. Invalid instruction exceptions require more processing in order for the program to complete execution normally. When an error is detected on a core, execution on both the cores is stopped and architectural state from the error- free core is copied onto the erroneous core. While resuming the processor, the execution sequence is altered on only the erroneous core (since PC is copied from error-free core). The error-free core resumes from where it was stopped]

---
Implementation details

---
Simulation setup: Outline
- Model a pic microcontroller PIC16F84A in C language
- Flip a bit in program memory and general purpose registers with a certain probability
  - Detect crashes/errors
- Implement an error correction algorithm (SECDED)
  - Note the improvement in error/crash rate

---
The complete flow
- Generate the assembly for PIC 16F84A from a C program using MPLAB IDE*
- Read instruction mnemonic from the assembly
- Instruction Fetch
- Instruction Decode
- Bit flip
  - Generate a random number using rand()
  - Flip a bit with a certain probability (0.6 to 1e-4)
- Check for program crash/error
- Instruction Execute
- Repeat the same program till a max number of crashes occur

---
PIC16F84A- Block diagram
Register file map
PIC16F84A Datasheet

---
Soft error- bit flips
SDC: Silent Data Corruption
DUE: Detected Unrecoverable Error
Process kill or System kill
The Soft Error Problem: An Architectural Perspective, (HPCA-11) 2005

---
Crash conditions
- Program counter changes
- Current instruction gets modified into a Control flow instruction (CALL/GOTO/RETURN)
- Unable to decode the instruction – Illegal opcode
- Access a prohibited memory location
- After a crash:
  - Note the instruction cycle at which the crash occured
  - Reset the system after each crash
  - Reload instructions to program memory and restart execution
- Calculate Mean time to failure (in terms of instruction cycles)

---
Error conditions
- Data being accessed by current instruction gets modified
  - Due to flipping of the content of memory location
  - Due to flipping of the data bit in the instruction itself
- Instruction in the program memory gets modified
  - Bit in the opcode has flipped (say, ADD becomes MOVE)
  - Destination bit has flipped (say, stores result in accumulator instead of memory)
  - Bit oriented instructions: Bit value flips (e.g., BCF: Bit clear function- ends up clearing bit 4 instead of bit 5)
  - Immediate value in the instruction changes (e.g., ADD 12, becomes ADD 13)
- Keep track of the number of errors

---
Hamming code
Single error correction, Double error detection: Code with Minimum Hamming Distance of 4
Constructing an Error Correcting Code,Andrew E. Phelps, University of Wisconsin, Madison
Encoding and Parity coverage
http://en.wikipedia.org/wiki/Hamming_code

---
SECDED- Hamming code
- Encode while writing instruction into program memory
  - Convert 8 bit register data into 13 bits
  - Convert 14 bit instruction into 20 bits
- Bit flip (flips the encoded content)
- Detect and correct error during Instruction Fetch (reading from program memory)
  - Decode the correct instruction
  - Continue normal execution
- Report crash only if Double error is detected
  - Repeat for a maximum number of crashes
- Calculate MTTF

---
Simulation results
1. Without Error correction

---
Examples: Histograms of crash events
Number of instruction cycles before each crash
Probability of bit flip= 0.1
Crash number
Instruction cycles
Number of instruction cycles before each crash
Probability of bit flip= 1e-2
Crash number
Instruction cycles
Calculating Mean time to failure (instruction cycles)

---
Mean time to failure (instruction cycles)
without error correction
Min, max and mean time to failure (instruction cycles)
Without error correction
Probability of bit flip
Instruction cycles before a crash
Max number of successful instruction cycles executed and still no crash
Only 1 crash in a day

---
Analysing the crashes
Categorising the crashes
(Without error correction)
Probability of bit flip
Percentage of the total crashes

---
Simulation results
1. With Error correction

---
Mean time to failure (instruction cycles)
With error correction
Crashes are only due to double bit errors
Min, max and mean time to failure (instruction cycles)
With error correction
Probability of bit flip
Instruction cycles before a crash
No crash in 2 days

---
Simulation time vs crashes
Total Simulation time vs number of crashes
(Without Error correction)
Probability of bit flip
Lower probabilities, more time for lesser number of crashes
Total simulation time vs number of crashes
(With error correction)
Probability of bit flip
Higher probabilities, less time for more number of crashes
No crash in 36 hours

---
Errors corrected using SECDED
Errors corrected using SECDED
Probability of bit flip due to soft error
Number of errors corrected

---
Future direction

---
Backup

---
PIC16F84A- Instruction set summary
General format of instructions
PIC16F84A Datasheet