Soft errors and reliability
Ph.D R&D Project
Nanditha Rao
under the guidance of
Prof. Madhav. P. Desai
Dept of Electrical Engineering
IIT Bombay
April 2012

---
Agenda
- Objective
- Soft errors and their impact
- Redundancy techniques
- Outline of the simulation setup
- PIC architecture in brief
- Implementation details
- Simulation results
- Conclusion

---
Objective
To study the impact of soft errors on processor execution and build reliability in the processor to reduce the impact

---
Soft error: physics
SDC: Silent Data Corruption
DUE: Detected Unrecoverable Error
A new physical mechanism for soft errors in dynamic memories,Timothy C. May, Murray H. Woods,Reliability Physics Symposium, 1978.

---
Soft errors
Impact of soft errors with technology generation
Modeling the Effect of Technology Trends on the Soft Error Rate of Combinational Logic, Premkishore Shivakumar, Proceedings of the 2002 International Conference on Dependable Systems and Networks
SDC: Silent Data Corruption
DUE: Detected Unrecoverable Error
Process kill or System kill
The Soft Error Problem: An Architectural Perspective, (HPCA-11) 2005

---
Hamming code
Single error correction, Double error detection: Code with Minimum Hamming Distance of 4
Constructing an Error Correcting Code,Andrew E. Phelps, University of Wisconsin, Madison
Encoding and Parity coverage
http://en.wikipedia.org/wiki/Hamming_code

---
Simulation setup: Outline
- Model a pic microcontroller PIC16F84A in C language
- Flip a bit in program memory and general purpose registers with a certain probability
  - Detect crashes/errors
- Implement an error correction algorithm (SECDED)
  - Note the improvement in error/crash rate

---
PIC16F84A- Block diagram
Register file map
PIC16F84A Datasheet

---
Instruction set summary
General format of instructions
PIC16F84A Datasheet

---
Implementation details

---
The complete flow
- Generate the assembly for PIC 16F84A from a C program using MPLAB IDE*
- Read instruction mnemonic from the assembly
- Instruction Fetch
- Instruction Decode
- Bit flip
  - Generate a random number using rand()
  - Flip a bit with a certain probability (0.6 to 1e-4)
- Check for program crash/error
- Instruction Execute
- Repeat the same program till a max number of crashes occur

---
Crash conditions
- Program counter changes
- Current instruction gets modified into a Control flow instruction (CALL/GOTO/RETURN)
- Unable to decode the instruction – Illegal opcode
- Access a prohibited memory location
- After a crash:
  - Note the instruction cycle at which the crash occured
  - Reset the system after each crash
  - Reload instructions to program memory and restart execution
- Calculate Mean time to failure (in terms of instruction cycles)

---
Error conditions
- Data being accessed by current instruction gets modified
  - Due to flipping of the content of memory location
  - Due to flipping of the data bit in the instruction itself
- Instruction in the program memory gets modified
  - Bit in the opcode has flipped (say, ADD becomes MOVE)
  - Destination bit has flipped (say, stores result in accumulator instead of memory)
  - Bit oriented instructions: Bit value flips (e.g., BCF: Bit clear function- ends up clearing bit 4 instead of bit 5)
  - Immediate value in the instruction changes (e.g., ADD 12, becomes ADD 13)
- Keep track of the number of errors

---
SECDED- Hamming code
- Encode while writing instruction into program memory
  - Convert 8 bit register data into 13 bits
  - Convert 14 bit instruction into 20 bits
- Bit flip (flips the encoded content)
- Detect and correct error during Instruction Fetch (reading from program memory)
  - Decode the correct instruction
  - Continue normal execution
- Report crash only if Double error is detected
  - Repeat for a maximum number of crashes
- Calculate MTTF

---
Simulation results
1. Without Error correction

---
Examples: Histograms of crash events
Number of instruction cycles before each crash
Probability of bit flip= 0.1
Crash number
Instruction cycles
Number of instruction cycles before each crash
Probability of bit flip= 1e-2
Crash number
Instruction cycles
Calculating Mean time to failure from these data

---
Mean time to failure (instruction cycles)
without error correction
Min, max and mean time to failure (instruction cycles)
Without error correction
Probability of bit flip
Instruction cycles before a crash
Max number of successful instruction cycles executed and still no crash
Only 1 crash in a day

---
Analysing the crashes
Categorising the crashes
(Without error correction)
Probability of bit flip
Percentage of the total crashes

---
Simulation results
1. With Error correction

---
Mean time to failure (instruction cycles)
With error correction
Crashes are only due to double bit errors
Min, max and mean time to failure (instruction cycles)
With error correction
Probability of bit flip
Instruction cycles before a crash
No crash in 2 days

---
Simulation time vs crashes
Total Simulation time vs number of crashes
(Without Error correction)
Probability of bit flip
Lower probabilities, more time for lesser number of crashes
Total simulation time vs number of crashes
(With error correction)
Probability of bit flip
Higher probabilities, less time for more number of crashes
No crash in 20 hours

---
Errors corrected using SECDED
Errors corrected using SECDED
Probability of bit flip due to soft error
Number of errors corrected