Fault models
- Memory faults:
  Static faults:
- Pin-fault- Stuck at fault (1/0),
- transition fault,
- address decoder fault,
- read faults (stuck-open faults)
  Dynamic faults- Single cell or two-cell dynamic faults
- e.g., Read followed by write RAW
- Pattern sensitive faults (memory contents affected by aggressor patterns- 5 or 9 aggressor)

---
Fault probability and test algorithm
Fault probability distribution
Fault coverage comparison for different algorithms.
March test algorithms provide complete coverage
- SAF: Stuck at fault- most occuring
- TF: Transition fault
- SOF: Stuck open fault
- CF: Coupling fault
- DRF: Data retention fault
Assessing SRAM Test Coverage for Sub–Micron CMOS Technologies,Vonkyoung Kim and Tom Chen, Colorado State University, VLSI Test Symposium, 1997., 15th IEEE

---
Probabilities of faults in Network on chips
Definitions used:
- Upon timing violation, a flit, that is, flow control digit (small packets of data) are written to a different random buffer (flit loss) potentially overwriting a useful flit latched there (data corruption).
- Also, since the buffer that the flit was intended for already sent a credit to the upstream router and not received the flit that used this credit, it assumes that the upstream router has not utilized this credit yet (credit loss).
- At system-level, the destination node will never receive the corresponding flit while, from now on, this buffer’s capacity is reduced by one flit buffer.
Methodology used:
Step 1. Static Timing Analysis to determine the critical paths
• Step 2. Extraction of critical paths with stressing inputs
• Step 3. Monte Carlo circuit-level simulations of critical paths to capture process-induced timing violations
• Step 4. Map circuit-level faults to system-level fault types
Enabling System-Level Modeling of Variation-Induced Faults in Networks-on-Chips
Konstantinos Aisopos†§ , Chia-Hsin Owen Chen§ , Li-Shiuan Peh§†
Princeton University § Massachusetts Institute of Technology, DAC 2011

---
Probabilities of faults in Network on chips
Definitions used:
- Upon timing violation, a flit, that is, flow control digit (small packets of data) are written to a different random buffer (flit loss) potentially overwriting a useful flit latched there (data corruption).
- Also, since the buffer that the flit was intended for already sent a credit to the upstream router and not received the flit that used this credit, it assumes that the upstream router has not utilized this credit yet (credit loss).
- At system-level, the destination node will never receive the corresponding flit while, from now on, this buffer’s capacity is reduced by one flit buffer.
Methodology used:
Step 1. Static Timing Analysis to determine the critical paths
• Step 2. Extraction of critical paths with stressing inputs
• Step 3. Monte Carlo circuit-level simulations of critical paths to capture process-induced timing violations
• Step 4. Map circuit-level faults to system-level fault types
Enabling System-Level Modeling of Variation-Induced Faults in Networks-on-Chips
Konstantinos Aisopos†§ , Chia-Hsin Owen Chen§ , Li-Shiuan Peh§†
Princeton University § Massachusetts Institute of Technology, DAC 2011

---
Importance of dynamic faults
Static Tests (S-Tests)- static faults
Diagnosis Dynamic tests- (DIag-D tests)- Single cell dynamic faults
Opt-D- optimised for certain single cell dynamic faults
SD-tests: Static and dynamic tests
Comparison of Static and Dynamic Faults in 65nm Memory Technology, Delft University of Technology and Intel Corporation, CiteSeerX - Scientific Literature Digital Library

---
Types of Fault injection
- Memory corruption: Fault injected in the task memory image and could remain throughout the program execution
- Spatial: Fault injection is triggered after N occurences of randomly chosen/user selected address
- Temporal: A built-in hardware time counts down to 0 and an error is injected everytime the timer resets to 0

---
Fault injection method
Temporal method resulted in the lowest error detection coverage
Temporal injection method would challenge the error detection
mechanisms to a higher degree
Reference: FERRARI: A Flexible Software-Based Fault and Error Injection System, IEEE TRANSACTIONS ON COMPUTERS, VOL. 44,NO. 2, FEBRUARY 1995

---
Redundancy schemes
- Error correction (Hamming code that can correct 1 to 3 bits whose value has been flipped)
- Triple modular redundancy with majority voting logic
- Checkpointing architectural states at regular intervals

---
Summary
- Dynamic faults are important and should be modeled over static faults
- TMR – temporal is a bigger challenge than spatial