Soft errors and reliability
Nanditha Rao
Dept of Electrical Engineering, IIT Bombay
nanditha@ee.iitb.ac.in

Abstract— Soft errors have become a reliability concern in today's process technology. The bit-flips in program memory can result in silent data corruption possibly leading to program crashes. Several mitigation techniques can be found in the literature. In this work, soft error impact is modeled at an architecture level in the form of bit-flips. The simulation results presented are for a 14-bit wide, 8k- program memory, simulated for a model of MicroChip PIC16F84A microcontroller. It is observed that SECDED (Hamming code) can improve the reliability or mean time to failure and prevent program crashes at lower probabilities of bit-flips.

Keywords—soft error, architecture, error correction, reliability
background of soft errors and reliability
Introduction
Technology scaling has made today’s designs more susceptible to soft errors. The lower supply voltages and nodal capacitances which are required for making circuits run faster, result in reduced critical charge (Qcrit- the amount of charge that distinguishes a zero from a one) required to flip a bit in digital circuits. The problem of Single Event Upsets (SEU) becomes more acute for aircraft and spacecrafts where high-energy neutrons at higher altitudes are abundant. Since it is predicted that soft error rate is increasing exponentially [1], it is crucial to consider soft error rate as an important design parameter and implement techniques to improve reliability. For high-end servers, and networking switches, reliability is even more important along with its performance. Several solutions have been employed for mitigating radiation effects ranging from process to architecture and circuit-level techniques. The micro-architectural solutions to mitigate SEU employ fault tolerant techniques such as Triple Modular Redundancy (TMR) and Error Detection and Correction codes for memory structures.
Soft errors
Soft errors in memory devices were first mentioned by May and Woods in 1978 [2]. They define "soft errors" to be random, non-recurring, single-bit errors. The errors are not permanent, i.e., they do not cause any physical defects. A bit-flip indicating a soft error is completely recovered by the following write cycle with no greater chance of showing an error than any other bit. The frequency at which these events occur is called the soft error rate (SER). In memory circuits or sequential logic, soft errors are caused by energetic particle strikes that generate enough free charge to upset the state of a latch or memory cell. In combinational logic, soft errors are caused by transient current or voltage spikes. They can either upset the clock timing or propagate and get latched at the output.
Causes of soft errors and the mechanism [15]:
Three major sources of soft errors have been identified. They are: alpha particles from package decay, cosmic rays creating high energy neutrons and thirdly, thermal neutrons.The alpha particles are doubly charged helium nuclei containing 2 protons and 2 electrons. They are released from high atomic- number atoms during radioactive decay, and then interact with other atoms due to their charge and high energy. The energy range emitted from all naturally occurring elements which undergo alpha decay ranges from 1 to 9 MeV. Alpha particles released from the decay of U-238, Th-232 in packaging materials can penetrate silicon devices to a depth of approximately 25 um.
The alpha particle:
A 5 MeV alpha particle impinging on a memory cell will produce 1.4 million electron-hole pairs in silicon to a depth of 25 μm [16]. Minority carriers are collected by the voltage across the depletion layer. The mechanism of a bit-flip due to particle strike is illustrated in Figure 1.
As the alpha particle passes through the semiconductor device, electrons are dislodged from the crystal lattice sites along the track of the alpha particle. If the total number of generated electrons collected by an empty storage well exceeds the number of electrons that differentiates between a 1 and a 0, the collected electron charge can flip a 1 to a 0 generating a “soft” (reversible) error in the memory device. This amount of charge that differentiates between a 1 and a 0 is called the critical charge, Qcrit (charge necessary to determine the cell state).

Figure 1: Stages of Soft Error Creation by Alpha Particles in Dynamic Memories [2].
 High energy neutrons:
At the Earth's surface approximately 95% of the particles capable of causing soft errors are a flux of energetic neutrons typically referred to as "cosmic rays" in the soft error literature. Neutrons are uncharged and undergo capture by the nucleus of an atom in a chip. This process may result in the production of charged secondary particles, such as alpha particles and oxygen nuclei, which can then cause soft errors.
Thermal neutrons:
Neutrons that have lost kinetic energy until they are in thermal equilibrium with their surroundings are another important cause of soft errors in some circuits. At low energies many neutron capture reactions become much more probable and result in fission of certain materials creating charged secondaries. Boron has been used in BPSG (Borophosphosilicate glass), the insulator in the interconnection layers of integrated circuits. For some circuits the capture of a thermal neutron by the nucleus of the Boron-10 isotope is particularly important. This nuclear reaction is an efficient producer of an alpha particle which may cause a soft error if produced in very close proximity, approximately 5 microns, to a critical circuit node.
CPUs in desktop computers run at a high enough Vcc that the Qcrit value is rarely exceeded by cosmic ray induced ionization. Cosmic ray intensity is 10 times worse at 2 Km above sea level and reaches a peak of approximately 300 times sea level at 10 Km [3]. Laptop computers are at risk in use during flights on commercial airlines, which typically fly at ~10 Km. The hazard to devices in laptop computers is further worsened by the smaller Qcrit value resulting from a low Vcc voltage used to reduce power consumption .
History and impact [5]:
In 1975, Binder, Smith and Holman demonstrated that electronic anomalies in communication satellite operation were due to cosmic ray particles with GeV energies and atomic numbers around 26. In 1976, the Cray-1 supercomputer installed at Los Alamos displayed ~25 non-permanent memory parity errors per month. Tthe source of these errors was not known, but in 2010, Normand and co-workers published a study showing the likely explanation was high energy neutrons from the cosmic rays [6]. In 1978, May and Wood studied the effects of alpha particles on RAM and CCD memory [2]. In 1979, Ziegler and Lanford published their study detailing the mechanisms whereby terrestrial cosmic rays could cause upsets in microelectronics. In the same year, Guenzer, Wolicki and Allas experimentally confirmed single event upsets (SEU) by irradiating 16K DRAM devices with 6.5 to 14 MeV neutrons and 32 MeV protons.
In 1995, Baumann and co-workers studied the effects of thermal neutron capture by Boron-10 in boro-phospho-silicate glass (BPSG). Their measurements showed a typical 600nm thick later of BPSG would generate ~0.02 events per are per hour.
Later, cosmic ray soft errors in SRAM cache modules used in Sun Microsystems servers caused excessive outages at various customer sites.

After the discovery of soft errors, semiconductor companies (Intel, IBM, Fujitsu), aerospace companies (Boeing, Ericsson-Saab Avionics), government organizations (Sandia National Labs, Jet Propulsion Laboratory, NASA) and universities initiated independent research programs.

Soft errors in various circuits:
Combinational circuits:
A particle that strikes a p-n junction within a combinational logic circuit can alter the logic value. A soft error in combinational logic is defined as a transient error in the result of a logic circuit that is subsequently stored in a memory circuit of the processor or is latched at the output.
A transient error in a logic circuit might not be captured in a memory circuit because it might be masked by one of the following three phenomena:
- Logical masking occurs when a particle strikes a portion of the combinational logic that is blocked from affecting the output due to a subsequent gate whose result is completely determined by its other input values.
- Electrical Masking occurs when the pulse resulting from a particle strike is attenuated by subsequent logic gates due to the electrical properties of the gates to the point that it does not affect the result of the circuit.
- Latching-Window Masking occurs when the pulse resulting from a particle strike reaches a latch, but not at the clock transition where the latch captures its input.

Memory and Sequential circuits:

Figure 2: Typical SRAM Cell [8]

Figure 2 shows a typical static RAM (SRAM) cell in an on-die memory. The word line (WL) is low, and the cell is holding its stored data using the back-to-back inverter configuration. The bitlines BL and BL# are decoupled from the memory cell by NMOS transistors. If a particle strike causes one of the nodes to undergo a transition, the disturbance may propagate forward through the inverter and cause a transient on the second node. Since the second node, in turn, drives the first node toward a wrong value, this regenerative action will cause both nodes to flip. Once the cell flips, there is no mechanism for its recovery other than explicitly rewriting the state via the bitlines. Similar state changes can occur in the sequential elements like latch or a register file.

Measurement of SER:
In the normal operation of a product, many environmental factors can cause errors: power supply noise, charge sharing, crosstalk, SEUs, etc. It is not easy to separate the sources of errors and identify a particle-induced soft error. One exception is measurement at high altitudes or on-board airplanes since the neutron flux increases by nearly three orders of magnitude at flight altitudes. Since a typical device SER is very low under normal conditions, it is more practical to measure the SER under accelerated conditions and then scale the measurements back to natural conditions. Although advances in packaging and fabrication have gradually reduced the effect of the alpha-particle induced SER, it remains important in SRAMs and DRAMs.

Technology scaling trends:
The scaling of process technology results in a simultaneous change of several parameters that affect the SER. Let us assume that supply voltage scales by a factor of K per generation, where K is 0.7. Then, the node capacitance scales as K, the node charge, critical charge and collection area scale as K2. As QCRIT decreases, the SER becomes worse. As the collection area decreases, the SER improves. In addition, the collection efficiency decreases with increased substrate doping and reduced bias voltage, which tends to reduce the SER. The net result of these compensating effects can be either an increasing or decreasing SER per cell.
Scaling in memories:

As illustrated in Figure 3, in scaling from one-megabit to one-gigabit technology, the DRAM single bit SER has been reduced by about four to five times per generation.

Figure 3: SER trends for DRAM as function of technology node [10]

  This continuous reduction is attributed to the shrinking junction volumes (lowering the collected charge), the relatively high node - capacitance, and the relatively gradual voltage scaling. While DRAM bit SER has been reduced by almost a 1000 times over six generations, the DRAM system SER has remained essentially unchanged. System memory requirements have increased (bits per system) nearly as fast as the SER reduction provided by scaling. Thus, DRAM system reliability has remained roughly constant over many generations. DRAM is one of the more robust devices in terms of soft error immunity. The only caveat to the DRAM SER trend is that as operating frequency is increased, soft errors in the bitline and sense amplifiers become dominant and DRAM SER is expected to increase with increasing frequency.

Figure 4: The system SER trend in SRAM devices as a function o f technology node [10]

In contrast, early SRAM was more robust against SER because of high operating voltages and the fact that data was stored as the state of a bi-stable circuit made up of two large cross-coupled inverters, each strongly driving the other to keep the bit in its programmed state. However, with each successive SRAM generation, reductions in cell collection efficiency due to the shrinking cell depletion volume have been swamped out by big reductions in operating voltage and reductions in node capacitance. Thus SRAM single bit SER increased with each successive generation, particularly in products using BPSG.
As feature sizes have been reduced into the deep sub-micron regime, the SRAM single bit SER has saturated [10]. This saturation in the single-bit SRAM SER is due to saturation in the voltage scaling (further reduction in operating voltage is limited by transistor threshold voltages), reductions in junction collection efficiency, and increased charge sharing due to short-channel effects with neighboring
nodes. Ultimately, as with DRAM, scaling also implies increased density, so saturation in S RAM bit SER does not translate to saturation in the system SER. As illustrated in Figure 4, the exponential growth in the amount of embedded SRAM in electronics has led the SRAM system SER to increase with each generation.

Scaling in latches:
The neutron SER dominates in latches due to a higher QCRIT than SRAM. It was projected that the SER per latch would increase by 10 percent per generation if voltage were scaled by 0.8x [11].

It is well known that as device voltage is reduced, the soft error rate increases due to the decrease in Qcrit [7]. This would imply that ultra-low power devices would suffer from higher soft error rates.
As feature sizes decrease, the number of transistors that can be placed on a ﬁxed size die increases quadratically, creating signiﬁcantly greater opportunity for soft errors. Since the rate of soft errors is different in SRAM cells, latches and logic, the SER of the processor will depend on the chip area devoted to each type of device.
Mitigation
A technical challenge of building reliable systems out of unreliable components is nothing new. For a system without redundancy, the probability of error-free operation decreases rapidly with increases in component count. Let us consider a microprocessor with about 1 billion transistors and an application that requires a mean time to failure (MTTF) of 100 years. To meet this requirement, a single transistor would have to reach an MTTF of 100 billion years. Several fault-tolerant techniques have been developed, especially for memories to meet such requirements. The difficulty is not in improving the reliability, but in doing it cost effectively and without degrading the speed or increasing the power consumption.
Process/Material improvements
The most obvious way to eliminate soft errors is to get
rid of the radiation sources that cause them. BPSG has been removed from many technologies to avoid the soft errors created by radiation from Boron-10 activation. In addition, alpha particle emission has been reduced by using pure materials, bumps physically separated from sensitive circuit components, and shielding chips with a thick polyimide layer prior to packaging [10]. While large reductions in SER are possible by these means, high-energy cosmic neutrons will always reach the devices and cause soft errors. Hence ultimately the SER is limited to a level defined by high-energy cosmic neutron radiation. SER can also be reduced by process adjustments, such as the use of buried barrier layers, multiple wells, or silicon-on-insulator (SOI)", but no process technology has yet been able to match the efficacy of properly designed error detection and correction approaches.

TMR:
 Triple modular redundancy (TMR) is a fault-tolerant scheme, in which three systems perform a process and that result is processed by a voting system to produce a single output. This architecture allows a soft error in a single logic path to be ignored since the other two are the majority and, thus, the correct data "wins" the vote. This method uses three times the chip area and reduces maximum operating frequencies since extra gate delays are introduced.

Error correction:
In its simplest form, error detection consists of adding a single bit to store the parity (odd or even) of each data word. If a single error has occurred, the parity check will reveal that the parity of the data does not match the parity hit. Thus this system allows for the detection of a single error at a minimal cost. The disadvantage is that the detected error cannot he corrected since the parity bit does not localize the error. In addition, if more than a single error has occurred the check will not reveal that anything is wrong, since the parity will match. The next and most common technique is Error Detection and Correction (EDAC) or Error correction code, ECC. This requires more parity bits to be assigned to each data word. For a 64-bit wide memory word, eight correction bits are required. These eight correction bits allow up to two errors to be detected and a single error to be corrected. Since most soft error events are single bit errors this protection scheme provides a significant reduction in failure rates but at a high cost in terms of design complexity, system latency, throughput, and chip area.

Checkpointing:
In checkpoint-based methods, the state of the computation as a checkpoint is periodically saved to a stable storage, which is not subject to failures. When a failure occurs, the computation is restarted from one of these previously saved states [12].

architecture model and implementation
PIC16F84A Architecture
Overview: The PIC16F84A belongs to the mid-range family of the PICmicro® microcontrollers. A basic block diagram of the microcontroller is shown in Figure 5.

Figure 5: PIC16F84A Block diagram [13]
- The program counter (PC) specifies the address of the instruction to fetch for execution. The PIC16FXX has a 13-bit program counter capable of addressing an 8K x 14 program memory space. For the PIC16F84A, the first 1K x 14 (0000h-03FFh) are physically implemented.
- The low byte of the PC is called the PCL register. This register is readable and writable. The high byte is called the PCH register which is updated through the PCLATH register.
- There are two memory blocks in the PIC16F84A: program memory and the data memory. The data memory can further be broken down into the Special Function Registers (SFR) area and the General Purpose Registers (GPR) area as shown in Figure 6.
- The SFRs control the operation of the device. Portions of data memory are banked. Banking requires the use of control bits for bank selection. These control bits are located in the STATUS Register. These registers are static RAM.
- Each General Purpose Register (GPR) is 8-bits wide and is accessed either directly or indirectly through the File Select Register (FSR).

Figure 6: PIC16F84A Register file map [13]

The stack allows a combination of up to 8 program calls and interrupts to occur. The stack contains the return address from this branch in program execution. Mid-Range MCU devices have an 8-level deep x 13-bit wide hardware stack.

Instruction set summary:

Each PIC16CXX instruction is a 14-bit word, divided
into an opcode, which specifies the instruction type
and one or more operands which further specify the
operation of the instruction. There are a total of 35 instructions in PIC16F84A.

The instruction set is grouped into three basic categories as shown in Figure 7: Byte-oriented operations , Bit-oriented operations , Literal and control operations. All instructions are executed within one single instruction cycle, unless a conditional test is true or the program counter is changed as a result of an instruction. In this case, the execution takes two instruction cycles with the second cycle executed as a NOP.

Figure 7: PIC16F84A General Instruction Format [13]

Implementation:
The microcontroller has been implemented in C language. A matrix multiplication program written in C was converted into assembly language of PIC16F84A using MPLAB Integrated Development Environment Software (IDE). The instructions in hex format were read from the file into an array. The program counter is initialised to the starting instruction. The next steps are: Instruction fetch, decode and execute. The program is executed continuously on the PIC model.
Fault model
Bits in the 8k program memory space and register file map of the PIC microcontroller model are randomly flipped at a certain probability ranging from 0.1 to 10-4. rand() function is used to generate a random number. The probability of occurrence of a certain number decides the probability of a bit flip amongst the 8k program memory space or the 256 register file locations. A bit flip is done after the decode stage, and before the execute stage.
Figure 8 shows the possible outcomes of a faulty bit in a processor.

Figure 8: Possible outcomes of a faulty bit [14]
SDC stands for silent data corruption and DUE for detected unrecoverable error.
Outcomes labeled 1-3 indicate non-error conditions. The most dangerous form of error is silent data corruption (SDC) (outcome 4), where a fault induces the system to generate erroneous outputs. To avoid SDC, error detection mechanisms, such as parity are employed. Simple error detection does not reduce the overall error rate, and are called detected unrecoverable errors (DUE). DUE events can be divided based on whether the detected error would have affected the final outcome of the execution or not. If they do not affect the outcome, they are called benign detected errors false DUE events (outcome 5 ) and others are true DUE events (outcome 6).
Conditions for a program crash/error:

Program crash:
Following a bit flip, either the instructions in the program memory or the data in the register file map will get modified. This is detected by comparing the random number generated using the rand() function with the memory locations being accessed by the program. Hence, during program execution, it is likely going to lead to an error or a program crash.

A program is said to have crashed if one of the following conditions are satisfied:
- If the program counter value changes, it is most likely going to lead to a crash atleast in a few instruction cycles
- Incorrect control flow: If the current instruction gets modified into a CALL/RETURN/GOTO instruction or if the CALL/GOTO location gets modified
- Illegal /memory access: If the memory location being accessed in the instruction gets flipped into some location which is reserved/illegal
- Illegal opcode

Following a crash, the system state is reset and the number of successful instruction cycles executed before the crash are noted. Instructions are reloaded into the program memory and execution is started afresh. This procedure is continued till around 15-20 crashes occur and the mean time to failure (MTTF) is calculated. This procedure is repeated for a range of probabilities of bit-flips (0.1 to 10-4) .

Program error:
On the other hand, a program error is said to have occurred if one of the following conditions are satisfied:
- Data being accessed by the current instruction gets modified either due to flipping of the content of memory location or due to flipping of the data bit in the instruction itself
- Bit in the opcode has flipped (say, ADD gets modified into MOVE instruction)
- Destination bit has flipped (say, stores result in accumulator instead of memory)
- Bit oriented instructions: Bit value flips (e.g., BCF: Bit clear function- ends up clearing bit 4 instead of bit 5)
- Immediate value in the instruction changes (e.g., ADD 12, becomes ADD 13)

A bit flip in a memory location is considered an error only if it is being accessed by the program and if it will affect the final outcome . An error would not lead to a program crash, and hence the machine state is not reset following an error but the execution is allowed to continue. However, the end result would be incorrect. The number of errors and the causes of errors are kept track of.

SECDED- Hamming encoding
Hamming codes are a family of linear error-correcting codes that generalize the Hamming(7,4)-code invented by Richard Hamming. Hamming codes can detect up to two and correct up to one bit errors. However, the simple parity code cannot correct errors, and can detect only an odd number of errors. Because of the simplicity of Hamming codes, they are widely used in computer memory (ECC memory). Extended Hamming codes achieve a distance of 4, by including an extra parity bit, which allows the decoder detect two bit errors. In this sense, extended Hamming codes are single-error correcting and double-error detecting, and are often referred to as SECDED.

Algorithm for Hamming encoding:
Figure 9 shows the general format of the Hamming encoded output.
Figure 9: Hamming encoding: Parity positions [13]
Following are the basic steps of the implemented algorithm:
- All bit positions that are powers of two are parity bits. All other bit positions are data bits.
- Each data bit is included in a unique set of 2 or more parity bits, as determined by the binary form of its bit position.
- Parity bit 1 covers all bit positions which have the least significant bit set: bit 1 (the parity bit itself), 3, 5, 7, 9, etc.
- Parity bit 2 covers all bit positions which have the second least significant bit set: bit 2 (the parity bit itself), 3, 6, 7, 10, 11, etc.
- Parity bit 4 covers all bit positions which have the third least significant bit set: bits 4–7, 12–15, 20–23, and similarly parity bit 8. The form of the parity is irrelevant, but even parity is mostly implemented.
During the very first step where the instruction is being read from the file and being written into program memory, it is encoded using the Hamming algorithm and written. During the instruction fetch stage, that is, when the instruction is being read from the memory, it is decoded and read. During this step, the parity bits are recalculated to detect an error. For example, if data bit 10 is in error, the parity bits 2 and 8 in the encoded data will be in error when re-calculated. Hence, summing up positions 2 and 8 will lead to 10, indicating that bit number 10 is in error. This erroreous data bit can be flipped, thereby correcting the error. Once the error is corrected, the correct data bits are extracted from the encoded data and used for the execution phase. The decoded data is again encoded back correctly and rewritten to the memory. The error is thus erased and will never propagate to the machine state.

Program crash:
In case of higher probability of bit-flips, there is a possibility of 2 bits flipping in the same memory location before it is actually being read and corrected by the decoder. This will result in double errors that cannot be corrected, but just detected. Such a case is reported as a program crash, since such errors cannot be corrected.
Simulation results
1. Without error correction
2. With error correction

Conclusions

 In this article,
References
1. P. Shivakumar, M. Kistler, S.W. Keckler, D. Burger, L. Alvisi, “Modeling the effect of technology trends on the soft error rate of combinational logic”. Dependable Systems and Networks, International Conference on 23-26 June 2002 Page(s):389 – 398
2. May, Timothy C. and Woods, Murray H., "A New Physical Mechanism for Sift Errors in Dynamic memories," IEEE- IRPS Proceedings, pp 33-40 (1978).
3. Ziegler, J.F, "Terrestrial Cosmic Ray Intensities," IBM J. of Res. Develop., Vol. 42, No. 1, January 1998
4. Robert C. Baumann , “soft errors in advanced semiconductor devices—part I: the three radiation sources”, IEEE transactions on device and materials reliability, march 2001
5. Slayman, C. , “Soft errors — Past history and recent discoveries”, Integrated Reliability Workshop Final Report (IRW), Oct 2010
6. E. Normand, J. L. Wert, H. Quinn, G. Grider, P. Iwanchuck, J. Morrison and S. Johnson, “First Record of Single Event Upset on the Ground, Cray-1 Computer Memory at Los Alamos in 1976”, IEEE Trans. on Nuclear Science
7. P. Hazucha, T. Karnik, J. Maiz, S. Walstra, B. Bloechel, J. Tschanz, G. Dermer, S. Hareland, P. Armstrong and S. Borkar, “Neutron Soft Error Rate Measurements in 90-nm CMOS Process and Scaling Trends from 0.25-um to 90-nm Generation,” Tech. Digest of the IEEE Electron Devices Meeting, pp. 21.5.1–21.5.4, Dec. 2003, San Francisco, CA
8. Karnik, T., “Characterization of soft errors caused by single event upsets in cmos processes ”, IEEE transactions on dependable and secure computing, vol. 1, no. 2, April-June 2004
9. J.F. Ziegler et al., “IBM Experiments in Soft Fails in Computer Electronics (1978-1994),” IBM J. Research and Development, vol. 40, no. 1, pp. 3-18, Jan. 1996.
10. Robert. Baumann, “The Impact of Technology Scaling on Soft Error Rate Performance and Limits to the Efficacy of Error Correction,” Proc. IEEE Int’l Electronic Device Meeting, pp. 329-332, Dec. 2002.
11. Y. Tosaka, S. Satoh, T. Itakura, H. Ehara, T. Ueda, G.A. Woffinden, and S.A. Wender, “Measurement and Analysis of NeutronInduced Soft Errors in Sub-Half-Micron CMOS Circuits,” IEEE Trans. Electronic Devices, vol. 45, pp. 1453-1458, July 1998.
12. Gengbin Zheng, Chao Huang and Laxmikant V. Kale, “Performance Evaluation of Automatic Checkpoint-based Fault Tolerance for AMPI and Charm++ ”,ACM SIGOPS Operating Systems Review, Volume 40 Issue 2, April 2006.
13. Microchip PIC16F84A Data Sheet
14. Shubhendu S. Mukherjee, Joel Emer, and Steven K. Reinhardt, “The Soft Error Problem: An Architectural Perspective ”, HPCA-11, 2005
15. L Lantz, “Tutorial- Soft errors induced by alpha particles”, IEEE Transactions on Reliability, 1996
16. SEMATECH Inc., “Semiconductor Device Reliability Failure Models ”, International SEMATECH May 31, 2000